## Slide 1
Design Specifications
Project Description
Areas of Impact
Wireless Neural Recorder
Yuan Gao, Tingkai Liu, Xin Huang, Stephen Xia
Department of Electrical and Computer Engineering, Rice University
Engineering Design for a Single Wireless Control Unit
Electrode Array
Wireless Control Unit Specifications
16 Channel Neural Electrode Sampling
Each channel needs to sampled at 1 kHz
Data fidelity: 8-bit Data Precision
Compact Form Factor: No larger than 15 x 15 x 15 mm
Operating battery life: > 24 hours
Analog Front-End
Intan RHD2000
    Specialized neural recording chip
    Protective circuitry
    Nanovolt precision
System Design Goal
To design a small, power-efficient wireless add-on to neural electrode.
Bluetooth Low Energy
Receiver
Secure Terminal
Communicates with the BLE transmitters on the probes
Data presentation and analysis
Prototype
Array of 16 electrodes
Each electrode outfitted with a wireless control unit (WCU)
Each WCU samples neural data and transmits in real-time to a secure terminal
Nordic NRF52
    6x6 QFN
    Upwards of 2 Mbits/s
    Compression
Acknowledgement
Next Steps
We would like to thank Dr. Gary Woods, Professor in the Practice of ECE, Rice University for his assistance and mentorship in guiding us through the product and technical development process; Dr. Aydin Babakhani, Assistant Professor of ECE, for his technical mentorship and support; Hamed Rahmani, Ph.D. student, for his technical mentorship and support; and Dr. Nitin Tandon, Neurosurgeon in the Texas Medical Center, for bringing the project into fruition and his support.
Special Thanks to the Brenner Foundation with Ellen Kirk and resources of the Oshman Engineering Design Kitchen. Without them, this project would not be possible.
PCB+ELECTRODE Images (When we get them)
Hospitals/Clinics
WiFi HaLow: Increase data rate beyond BLE products
Custom IC: ideally should fit within 8 x 8 x 8 mm
Begin animal testing with functional prototype
Households
Research Institutions
Currently, no solution exists on the market for an efficient recording of neural brain activity that is not restricted by a physical tether. Our project goal is to develop a low-power wireless recording device that digitizes neural signals from a 16-channel, 16-element electrode array and send the neural data wirelessly to a portable receiver. The wireless neural recorder will first be wireless embedded ECoG system implemented in animals and eventually humans.