## Slide 1: WNR Weekly Meeting
February 4, 2016

## Slide 2: Agenda
Compression Buffers
Wireless
  BLE
  Bluetooth
  Constraints
Analog Front-End

## Slide 3: Constraints - BLE: Nordic NRF52
Power Consumption:
  Transmission at +0 dbm: 5.5 mA
  Total Consumption = 5.5 mA * 24 hours = 132 mAh for 24 hours
Application Throughput
  ~250 kbps
Size
  6 x 6 mm

## Slide 4: Constraints - BT: CC2564 + MSP430F5438
Power Consumption:
  CC2564 Best Case: 10 mA -> 240 mAh for 24 hours
  MSP430 F5438 LPM4: 14.5 uA -> .348 mAh for 24 hours
  Total Consumption = 240.348 mAh for 24 hours
Application Throughput:
  0.7 ~ 2.1 mbps
Size:
  MSP430 F5438: 14 x 14 mm
  CC2564: 8 x 8 mm
  Constraining size = 14 x 14 mm

## Slide 5: Parameters and Required Throughput
Precision: 8-bit
Sampling Rate per channel: 1 ks/sec
Channels per probe: 16
Probes per array: 16
Total Bandwidth required: 2 Mbps
  To use BLE we need a factor of 8 decrease