## Slide 1: WIRELESS NEURAL RECORDER
Helping 70 Million Epilepsy Patients in THE WORLD

## Slide 3
1% | 10 - 25 Million
5 - 6 Days | 

## Slide 4: CUSTOMERS – EEG service providers
Hospitals | Clinics | Research Institutes
4000 | 5000 | 150

## Slide 5: Total Market Value
Customers * Machines * Unit Price
                ~ $ 300 Million

## Slide 6: Customer need
Safety & HIPAA
Convenience & Mobility
Accuracy & Reliability
Application development platform

## Slide 7: Existing product (NEuronexus)

## Slide 8: DEUTERON’s Smallest wireless neural logger
For animal applications
Size is still not ideal
Not Real-Time

## Slide 9: Design Specifications
Safe
  Skin Temperature Change: < 2C
  DC Offset: no feedback current

## Slide 10: Design Specifications
Real-Time Data Collection
  Transmission Rate: 128 kB/s
  Sampling Rate: 1 kHz

## Slide 11: Design Specifications
Accurate and Comprehensive Data
  Sampling Precision: 16-channel, 8-bit
  Sampling Rate: 1 kHz

## Slide 12: Design Specifications
Low Power and Long-Lasting
  Battery Life: >= 24 Hours
  User Replaceable/Rechargeable

## Slide 13: Design Specifications
Portable/Convenient/User Friendly
  Module Size: 4 x 4 mm
  3 meter Operational Radius

## Slide 14: System Diagram

## Slide 15: Challenges
Data Transmission
Power
Safety

## Slide 16: Wireless Options
5 Potential Options for Wireless Data Transfer
  Bluetooth Low Energy
  Wifi 2.4 / 5 GHz
  Other RF Bands
  Zigbee
  NFC

## Slide 17: Wireless Options
5 Potential Options for Wireless Data Transfer
  Bluetooth Low Energy
  Wifi 2.4 / 5 GHz
  Other RF Bands
  Zigbee
  NFC

## Slide 18: Bluetooth Low Energy
Most likely use BLE as our transmission source with a TI CC2640 BLE 4.2
Industry-leading privacy. Keeps Bluetooth Smart devices from being tracked.
Highly secure. Features industry-standard encryption ensuring confidential data stays that way.
More power efficient. Introduces refinements that make Bluetooth Smart even more power-stingy.

## Slide 19: Power Options
Powering the electrode is a huge challenge due to size and longevity constraints
2 Options
  High density replaceable medical device batteries
  Inductive charging via brain’s electrical impulses

## Slide 20: Power Options
Powering the electrode is a huge challenge due to size and longevity constraints
2 Options
  High density replaceable medical device batteries
  Inductive charging via brain’s electrical impulses

## Slide 21: Prototype Plan
3 Stages of prototyping with testing and iterating
  Stage 1
    Single electrode circuit prototype testing BLE technology with generated signals from oscilloscope
  Stage 2
    Multiple electrodes prototype to test multi-system communications
  Stage 3
    Full 16 electrode system with mobile recording device and animal testing

## Slide 22: Wireless Neural Recorder
Applications not only limited to epilepsy
  Sleep diagnosis
  Diagnosis diseases of the brain
  Coma analysis
  Brain stimulation
Improve Epilepsy patients’ quality of life
  Untether them from the limitation of existing technology
  Improve monitoring with more data for better procedural